## Slide 1: What the heck is a Raspberry Pi?
Rolfe Bozier
10-Dec-2014

## Slide 2: Agenda
Background
Hardware
Getting started
What can you do with it?
Some demos
Giveaway!

## Slide 3: Overview
Credit-card sized computer
Created to promote basic computer science in schools, inspired by Acorn BBC Micro (c. 1981)
Low cost ($20-35)
Designed by Eben Upton, a Broadcom employee
Managed by Raspberry Pi Foundation - not for profit
First released Feb 2012
Extremely popular (current sales of 3.8 million in < 3 years)

## Slide 4: Hardware
Broadcom BCM2835 SoC
  ARM1176 700MHz 32-bit CPU
  VideoCore iV GPU
  256-512MB RAM
Optional 10/100 ethernet port
1-4 USB 2.0 ports
SD / microSD slot
HDMI and/or composite video out
Analogue audio out, HDMI out, I2S in/out
GPIO pins including: UART, I2S, I2C, SPI, power
MIPI camera connector

## Slide 5: Hardware

## Slide 6: Hardware
Comparison
  CPU ~ 300MHz Pentium II (1997-99 vintage)
  GPU ~ 2001 XBox
Models
  Model A+ - 256MB RAM, 1 USB, 200mA - $23
  Model B+ - 512MB RAM, 4 USB, 1 10.100 ethernet, 600mA, more GPIO - $38
  Model A - obsolete version of A
  Model B - obsolete version of B
  Compute module - less dedicated I/O, more GPIO, SO-DIMM format

## Slide 7: What does it run?
Linux:
  Raspbian (Debian), Pidora (Fedora), Arch, Gentoo, openSUSE
Other OSs:
  RISC OS, FreeBSD, NetBSD, Plan 9, Inferno
Application-specific:
  OpenWrt, Xbian, XBMC, Instant WebKiosk
Not Windows 
Applications:
  Mathematica, Minecraft
Linux development tools
  gcc compiler (C, C++)
  Python, perl
  Scratch
  of course you can download and install many more

## Slide 8: Getting started
What you typically need:
  USB keyboard + mouse
  Monitor with HDMI video in
  5V power supply via micro USB
  Network connection (ethernet or wifi dongle)
  micro SD card with bootable OS (or install image)
Typical install image is "NOOBS"
  contains install images for Arch, Pidora (Fedora), Raspbian (Debian), XBMC
  you can choose which image[s] to install
  Takes around 20 minutes
  System runs entirely from the SD card

## Slide 9: Installation process
Initial install process
  insert SD card and apply power
  choose install OS[s]
  reboot
  set up some initial config (keyboard, hostname, locale, sshd server etc.)
  reboot
  You’re done
There are a huge number of resources on the Internet to get you started

## Slide 10: Now what?
What can you do with it?
  Learn some Linux sysadmin
  Use it as a low-power network server (e.g. DHCP, DNS, NTP, print server, ...)
  Run a dedicated application on it (e.g. kiosk, XBMC media centre, security camera)
  Use it as an experimental Linux platform
  Home automation
  Programmable camera
  Hook it up to some hardware to make it more widely accessible
  Christmas light controller
  Robot controller
  Add extra HAT boards on to it
  Build a radio-astronomy interferometer

## Slide 11: Fingers crossed…
Demos
  Sensor network receiver
  Smart still / video camera
  Software-defined radio receiver