## Slide 1: A trip down memory lane
Rolfe Bozier
16-Sep-2015
(or, all about core memory)

## Slide 2: Agenda
What did core memory look like?
Its place in computing history
How did it work?
A proof-of-concept

## Slide 3: What does core memory look like?
1 bit stored in a small ferrite ring
This array:
  16 kwords = 32 kbytes
  294,912 cores
  72 sub-blocks of 4 kbits
Separate driver board
Manufactured around 1977
  General Automation Inc
҉
Notes: Ferrite cores
Core array

## Slide 4: What does core memory look like?
Sub-block:

## Slide 5: A brief history of computer memory
Before core memory
  Relays
    10-100s of bits
  Rotating magnetic drums (1932 – 1960s)
    Up to 100s kbits
    Sequential access
    Ancestor of floppy / hard disks
  Williams tube (1947 - mid 1950s)
    1-2 kbits
    Random access
  Delay lines (1947 – mid 1950s (and beyond))
    1 kbit
    Sequential access
After core memory
  Semiconductor integrated circuits (early 1970s – now)
҉
Notes: What was it replaced by? DRAM bank, flash cards

## Slide 6: A brief history of computer memory
The lifetime of core memory, around 20 years

## Slide 7: How did it work?
Ampere’s Law: A current generates a magnetic field encircling the wire
Place a ferromagnetic ring around the wire and the magnetic field can induce a permanent magnetic field in the ring
  Clockwise = 0
  Anti-clockwise = 1
So we can store 0 and 1 values in a ferrite ring, but how can we read the value back?

## Slide 8: US 2,708,722 – An Wang
Magnetic field in the ring is not proportional to the current
Faraday’s Law: change in magnetic field induces a current in a nearby conductor
  Add a second “sense” wire through the ring
  Sense wire detects the flip as a pulse

## Slide 9: US 2,708,722 – An Wang
Destructive read:
  Write “0” value
  If sense wire detects a flip,
    The previous value was “1”
    Rewrite the “1” value back
  otherwise, do nothing
  Wang created a 50-bit shift register form of memory using this technique
In 1955, Wang sold the patent to IBM for $500,000
  That’s about $4.5M in today’s money…
  Wang went on to form Wang Laboratories and revolutionise office computing

## Slide 10: US 2,736,880 – Jay Forrester
Split the current through a ring across 2 wires; total current = threshold value
Arranges cores in an X/Y array
  Pass half the current through 1 column
  Pass half the current through 1 row
  Only the core at the intersection gets the right amount of current
Only need address lines
1 sense wire going through all cores
Random access
In 1964, MIT sold the patent to IBM for $13,000,000
  That’s about $100M in today’s money

## Slide 11: Into the third dimension
You can’t keep making arrays bigger and bigger
Stacking them makes sense
  Expand the address space by using extra bits to address each plane
  Store each bit of a word in a separate plane
The inhibit wire was added to make this easier
  Goes through each for in the plane (like the sense wire)
  All planes share the same address lines
  If you don’t want to write to a plane, put some reverse current through the inhibit line, so the net current is below the threshold
҉
Notes: Show driver board

## Slide 12: Performance
Performance
  10s of kBytes per plane
  Access time < 1μs (clock rate > 1MHz)
  Random access
  Non-volatile
  Power-hungry
Assembly
  Manual at first
  Eventually jigs were created for semi-manual assembly
    Shaking, vacuum tables
    Wires threaded with special needles
  “Ferrite Core Planes and Arrays: IBM’s Manufacturing Evolution”
    http://ibm-1401.info/IBMCoreArraysIEEEMagnetics1969.pdf

## Slide 13: Proof-of-concept
You can buy ferrite cores on eBay:

## Slide 14: Proof-of-concept
An 8 byte memory board:
҉
Notes: Memory board

## Slide 15: Proof-of-concept
Detecting the sense line pulse:

## Slide 16: Questions?
?