## Slide 1: Embedded Software Development
Rolfe Bozier
20-Feb-2014

## Slide 2: Introduction
Many of us write software that ends up in an embedded system, but...
  what is an embedded system exactly?
  how does my software fit in?
  what are the ramifications for what we write?
What is an embedded system?
  "A software environment often of limited functionality which is created for a special purpose"
A continuum ranging from tiny 8-bit micro-controllers up to systems approaching general purpose computers
Lots of examples: cars, toys, appliances, printers, cameras, watches, phones, ...

## Slide 3: Evolution of embedded systems - 1
Microprocessor-based systems
Separate ICs for:
  CPU, ROM (software), RAM, Interface logic
Processors: Z80, 68000, 8088+
Look like desktop computers from 30-40 years ago

## Slide 4: Evolution of embedded systems - 2
Micro-controller based systems
uC (CPU, ROM, RAM, I/O)
Single IC containing:
  CPU, Flash RAM (software), RAM, I/O controllers
Range from tiny 8-bit devices to medium-sized 32-bit devices

## Slide 5: Evolution of embedded systems - 3
Programmable/custom hardware
Single IC containing your choice of:
  CPU[s], ROM (software), RAM, Interface logic
  You choose clock speed, complexity etc
  Common processors: ARM, SPARC, MIPS, 8051, MSP430
Team up with large external RAM, ROM, Flash for more capable systems
FPGA - programmable hardware
  A large array of general purpose logic elements that can be configured to implement processors, memory banks, interfaces etc
  extremely flexible
ASIC – custom hardware
  take your hardware model and fabricate it in silicon
  minimize size (cheaper) but higher up-front cost

## Slide 6: Examples
Wireless temperature sensor
  2K Flash, 128b RAM, 8-bit @ 3.68MHz
KVM
  Xilinx FPGA, Xilinx CPLD
  Atmel microcontroller (4K Flash, 8-bit @ 8MHz)
  Renasas microcontroller (128K Flash, 32-bit @ 20MHz)
  Flash, 2 X SRAM
  Logic

## Slide 7: Examples
Brother printer (HL-1270N - 1999)
  ASIC (SPARClite core @66MHz)
  1MB ROM (software), 4MB RAM
Brother printer (HL-1650 - 2001)
  ASIC (SPARClite core @ 96MHz, bus I/F etc)
  16MB ROM (software), 2MB Flash, 8MB RAM
Canon printer (MG5560 - 2013)
  ASIC (ARM + Relax cores, ROM (software), bus I/F)
  32MB Flash (more software), 128MB RAM

## Slide 8: Impact on the developer
Processor can be limited
  slow clock speed (< 1GHz)
  small word size (32, maybe 16 or even 8)
  probably no FPU
  no MMU -> no memory protection
  usually stuck with assembler or C/C++
  the compiler may have some "issues"
  performance is going to be slower (maybe an order of magnitude)
  watch out for operations that have to be emulated
    divide / modulus
    floating point
    operations larger than word size
  you can finally use volatile for its intended purpose!

## Slide 9: Impact on the developer
ROM space limited
  get rid of unnecessary code
  restructure code to let the linker drop unrequired objects
  maybe replace a set of optimised functions with a single, slower version
  don't drag in unnecessary code from the OS support library
  forget about the POSIX API

## Slide 10: Impact on the developer
RAM space limited
  128B through to 10s of MB
  no virtual memory
  no heap (malloc)
  no high-level languages, no recursion
  think about how much memory you need
  think about how much memory you really need:
    Global data – pre-allocated at startup
    Stack data (local variables, function arguments) grows from one end of memory
    Heap data (malloc) - if you have one - grows from the other
    What happens when they collide? There is likely no protection

## Slide 11: Impact on the developer
System issues
  small or non-existent caches
  maybe you don't get cache coherency
No/limited OS
Cooperative multitasking rather than pre-emptive multitasking
Maybe no parallel threads
No keyboard, mouse, display, filesystem, disk, ...
Debugging much harder
  Simulate the system instead
  Dig out the logic analyzer!

## Slide 12: Why do it then?
Cost
  If you’re going to sell millions of units, embedded systems are cheaper
  Cheaper to move costs from hardware (per unit) to software (one-off)
Real-time!
Hardware/library support for useful stuff
  serial I/O, USB, timers, ADCs, ...
  high-speed bulletproof I/Fs (PCI, Ethernet, etc)
Low footprint (physical size, power requirements)
Security