## Slide 1: How the Internet works
Rolfe Bozier
3-Apr-2014

## Slide 2: An introduction to TCP/IP protocols
What happens when I type "http://www.google.com/" in my browser?
Why do I care?
  developing a distributed system
  debugging a distributed system
  why can't I connect to a remote service?
  how would I connect two system together?
  how can I tell what is happening behind the scenes?

## Slide 3: Packets and protocols
Data is exchanged between computers in "packets"
  A packet usually comprises a header and a payload
  Packets can be nested - a payload can contain another packet, with its own header and payload
  Packet headers have a well-defined structure and content
A protocol is a definition of a set of packet layouts and how they are exchanged
Because packets can be nested, a protocol can encapsulate another protocol (and so on)
  This nesting of protocols allows us to extend a protocol to support more features and functionality
Packets are good for a number of reasons:
  easy to manage latency
  easy to spread / balance load
  error recovery is more efficient

## Slide 4: The Internet runs on the TCP/IP protocol suite
The Internet is built on a hierarchy of protocols known colloquially as TCP/IP
We will cover the following in this talk:
Protocol Hierarchy |  |  | OSI model
 | DNS | HTTP | ???
 | UDP | TCP | Transport layer?
ARP | IP |  | Network layer
ethernet |  |  | Data link layer

## Slide 5: The lowest level (that we will consider)
I will assume that we have a "data link" layer between your computer and the rest of the world (usually a network switch)
  typically this is an ethernet link
  or maybe PPP over a dialup or DSL line
Each end has a "link address" (e.g. MAC / hardware / ethernet address)
There is an electrical connection between the two ends
Each end can send bytes to the other (maybe at the same time)

## Slide 6: Ethernet packets
src addr is the MAC address of your computer
dst addr is the MAC address at the other end of the cable (on your local network)
To send this packet, just send it down the wire (final delivery is not your problem!).
Ethernet is a broadcast medium.
Historically:
  everyone on the same piece of coax (don't break it!)
  Later, hubs allowed people to connect/disconnect but it was still broadcast
  Today, bridges/switches partition the network into segments; these devices know which way to pass on a packet
The address space is still flat
src addr | dst addr | type | payload

## Slide 7: Separating addressing from hardware - ARP
MAC addresses don't scale or allow partitioning
IP addresses are hierarchical: A.B.C.D
  prefix part is network ( e.g. 192.168.20 )
  rest is host ( .100 )
Each host is assigned an IP address
Linking IP addresses to hardware addresses is done by the ARP protocol
An ARP request leaves one of the last 2 fields blank and broadcasts it to the entire local network
A destination that recognises its ether/IP address sends a reply back to the src ether address with the missing details
The original host now knows the matching ether address for an IP address
  Replies are cached for a while for efficiency
  If no reply, try a few times then give up
ether hdr | src ether addr | src IP addr | dst ether addr | dst IP addr

## Slide 8: Direct host-host communications - IP
Now we can talk with other computers using IP addresses
But the ethernet header contains the dst ether address, so why do we need a dst IP addr?
  IP networks can span beyond your local network
  routers can manage the exchange of packets between networks
IP addresses are hierarchical, so we can efficiently route networks:
  send all packets for 203.8.* to *that* router over there
  send all unknown addresses to your internet router
We can address another IP host using the IP protocol:
The IP protocol also handles:
  fragmentation / reassembly when your data is bigger than the max packet size
  checksums for error detection
  time-to-live - expire packets if they travel too far (e.g. in a loop)
  what protocol is encapsulated within the payload?
Now we can send a packet to an IP address, but what happens to it there?
ether hdr | header | src IP addr | dst IP addr | payload

## Slide 9: Direct host-host communications - IP
Now we can talk with other computers using IP addresses
But the ethernet header contains the dst ether address, so why do we need a dst IP addr?
  IP networks can span beyond your local network
  routers can manage the exchange of packets between networks
IP addresses are hierarchical, so we can efficiently route networks:
  send all packets for 203.8.* to *that* router over there
  send all unknown addresses to your internet router
We can address another IP host using the IP protocol:
The IP protocol also handles:
  fragmentation / reassembly when your data is bigger than the max packet size
  checksums for error detection
  time-to-live - expire packets if they travel too far (e.g. in a loop)
  what protocol is encapsulated within the payload?
ether hdr | header | src IP addr | dst IP addr | payload

## Slide 10: Host and domain names
IP addresses are fine technically, but not much good for people
  Host and domain names are a human-friendly hierarchical naming system
  Matching IP addresses to hostnames is done by the DNS protocol
  DNS is a UDP-based protocol on top of IP
UDP - datagram protocol
  sometimes you may want to send one packet, maybe with a reply
The dst port controls which service will process the packet at the dst
  The src port allows for replies
  UDP is stateless, not guaranteed, unordered
  But it is useful if you can tolerate lost packets, for broadcasts, or if you don't really care
ether hdr | IP hdr | header | src port | dst port | other | payload

## Slide 11: DNS – domain name system
Name / address lookup is provided by DNS servers
  typically you start by querying a local DNS server
The requestor provides the requests, and server fills in the answers
DNS uses UDP, so packets may get lost
The protocol allows for retries and failover to alternate servers
DNS servers can be very busy, so a lightweight protocol is good
Now we can talk with other computers using host names
ether hdr | IP hdr | UDP hdr | request[s] | reply[s]

## Slide 12: Talking to web servers
A visit to a web page in your browser typically involves the exchange of a lot of different types of data (web pages, style sheets, images, forms etc)
  So UDP is not really appropriate
HTTP is a TCP-based protocol on top of IP
TCP is a protocol that provides connection-based communications
  A TCP connection is a long-lived conversation between two hosts with two-way traffic
The dst port specifies which service will process the packet at the dest
  Replies are sent back to the src port
TCP is reliable, ordered, guaranteed (the TCP protocol looks after this for you)
You can assume the packets you send are not lost and are received in order
Before you can start, you must exchange 3 initiation packets
ether hdr | IP hdr | header | src port | dst port | seqno | ackno | flags | payload

## Slide 13: The HTTP Protocol
HTTP is the protocol for interacting with web servers
Note that unlike the other protocols we have looked at, HTTP is a text-based protocol
  “GET /index.html HTTP/1.0”
ether hdr | IP hdr | TCP hdr | Request or reply

## Slide 14: Putting it all together
Open www.google.com in a browser
We need to turn www.google.com into an IP address
We need to connect to our local domain server, 192.168.13.6
We need to get the MAC address for this address:
Broadcast an ARP request for 192.168.13.6's MAC address
Receive ARP reply
Send a DNS request to the DNS server's MAC address for www.google.com
Receive DNS reply saying it is at 203.8.170.1
This is outside our network, so it must go via our gateway, 192.168.13.1
Broadcast an ARP request for 192.168.13.1's MAC address
Receive ARP reply
Establish 3-way TCP handshake with 203.8.170.1 via our gateway MAC address
Send TCP SYN to port 80 on 203.8.170.1
Receive TCP SYN+ACK
Send TCP ACK to port 80 on 203.8.170.1
Send HTTP request to port 80 on to 203.8.170.1: "GET /index.html HTTP/1.0"
Receive HTTP reply containing HTML data
etc

## Slide 15: Summary
Packet-based protocols are very flexible
  TCP/IP has been around for over 40 years
  There are literally thousands of protocols based on it
Once you understand the basic protocols we have covered, the rest is just details
If you want to know more:
  Anything by Richard Stevens is very readable
  RFCs are Internet standards that define protocols exactly